Form Factor for a spherical vesicle with two aligned curved domains

The form factor is calculated by taking the form factor of a flat-capped sphere (Sasfit manual p.47) of radius r (1) away from that of a second capped sphere with radius r+tsh (2), both with equal scattering length densities, then subtracting the cylindrical caps on each end (3,4) and adding cylindrical caps with the same radius but a different thickness and different scattering length densities (5,6). Lastly, we must add the outer curved cap of the domain with a different radius of curvature to the main sphere (one on each side) (7,8), and subtract an inner curved cap from each side (9,10).

Flat-capped sphere of radius r:

matrix { F_r^CS # "=" ~%DELTA%eta_sh int from -{r cos%theta_2} to {r cos%theta_1} dz int from 0 to sqrt{r^2 - z^2} {%rho d%rho} int from 0 to {2%pi} d%phi ~ e^{i vec Q cdot vec r}##{}# "=" ~%DELTA%eta_sh ~ 2%pi int from -{r cos%theta_2} to {r cos%theta_1} dz int from 0 to sqrt{r^2 - z^2} {%rho d%rho} ~ e^{iQz cos%psi}~ J_0 (Q%rho sin%psi) ##{}# "=" ~%DELTA%eta_sh ~ 2%pi int from -{r cos%theta_2} to {r cos%theta_1} dz ~ e^{iQz cos%psi} ~[r^2 - z^2] ~{J_1(Q sqrt{r^2 - z^2} sin%psi)} over {Q sqrt{r^2 - z^2} sin%psi} }

where vec Q ~ = ~ Q ~ left( stack { 0 # sin%psi # cos%psi } right) , and vec r ~ = ~ left( stack { %rho cos%phi # %rho sin%psi # z } right)

Flat-capped sphere of radius r+tsh:
F_{r+t_sh}^{CS} "=" ~%DELTA%eta_sh ~ 2%pi int from -{(r+t_sh)cos%THETA_2} to {(r+t_sh)cos%THETA_1} dz ~ e^{iQzcos%psi} ~ [(r+t_sh)^2 - z^2] ~ {J_1 (Q sqrt{(r+t_sh)^2 - z^2}sin%psi)} over { Q sqrt{(r+t_sh)^2 - z^2}sin%psi}

where %THETA_1 ~=~ arcsin` left({r sin%theta_1} over {r+t_sh}right) , and %THETA_2 ~=~ arcsin` left({r sin%theta_2} over {r+t_sh}right)

Cylindrical cap (right):

matrix { F_rt^CC # "=" ~%DELTA%eta_sh int from {r cos%theta_1} to {(r+t_sh)cos%THETA_1} dz int from 0 to {r sin%theta_1} %rho d%rho int from 0 to {2%pi} d%phi ~ e^{i vec Q cdot vec r} ##{}# "=" ~%DELTA%eta_sh int from {r cos%theta_1} to {(r+t_sh)cos%THETA_1} dz int from 0 to {r sin%theta_1} %rho d%rho int from 0 to {2%pi} d%phi ~ e^{iQ (%rho sin%phi sin%psi + z cos%psi)} ##{}# "=" ~%DELTA%eta_sh ~ {2%pi} int from {r cos%theta_1} to {(r+t_sh)cos%THETA_1} dz int from 0 to {r sin%theta_1} %rho d%rho ~ J_0 (Q%rho sin%psi) ~ e^{iQz cos%psi} ##{}# "=" ~%DELTA%eta_sh ~ {2%pi} ~ {J_1 (Qr sin%theta_1 sin%psi)} over {Q sin%psi} int from {r cos%theta_1} to {(r+t_sh)cos%THETA_1} dz ~ e^{iQz cos%psi} ~ ##{}# "=" ~%DELTA%eta_sh ~ {2%pi} ~ {J_1 (Qr sin%theta_1 sin%psi)} over {iQ^2 cos%psi sin%psi} left[e^{iQz cos%psi} right]_{r cos%theta_1} ^{(r+t_sh)cos%THETA_1} ##{}# "=" ~%DELTA%eta_sh ~ {4%pi i} ~ {J_1 (Qr sin%theta_1 sin%psi)} over {Q^2 sin(2%psi)} ~ lbrace {exp[iQr cos%theta_1 cos%psi] - exp[iQ(r+t_sh )cos%THETA_1 cos%psi]} rbrace }

Cylindrical cap (left):

F_l^CC ~"=" ~%DELTA%eta_sh ~ {4%pi i} ~ {J_1 (Qr sin%theta_2 sin%psi)} over {Q^2 sin(2%psi)} ~ left lbrace {exp[-iQ(r+t_sh)cos%THETA_2 cos%psi] - exp[-iQr cos%theta_2 cos%psi]} right rbrace

Domain cylindrical cap (right):

F_rt^DC "=" %DELTA%eta_d {4%pi i} {J_1 (Qr sin%theta_1 sin%psi)} over {Q^2 sin(2%psi)} left lbrace {exp[iQ((r+t_sh) cos%THETA_1 - l_1) cos%psi] - exp[iQ(r+t_sh) cos%THETA_1 cos%psi] } right rbrace

Domain cylindrical cap (left):

F_l^DC "=" %DELTA%eta_d {4%pi i} {J_1 (Qr sin%theta_2 sin%psi)} over {Q^2 sin(2%psi)} left lbrace {exp[-iQ(r+t_sh) cos%THETA_2 cos%psi] - exp[-iQ((r+t_sh) cos%THETA_2 + l_2)cos%psi]} right rbrace

Domain outer curved cap (right):

matrix { F_rt ^OC # "=" ~%DELTA%eta_d int from {(r+t_sh) cos%THETA_1} to R_1-d_1 dz int from 0 to sqrt{R_1^2 - (z+d_1)^2} %rho d%rho int from 0 to {2%pi} d%phi ##{}# "=" ~%DELTA%eta_d ~ 2%pi int from {(r+t_sh) cos%THETA_1} to R_1-d_1 dz ~ e^{iQz cos%psi} ~ [R_1^2 - (z+d_1)^2]~ {J_1 (Q sqrt{R_1^2 - (z+d_1)^2} sin%psi)} over {Q sqrt{R_1^2 - (z+d_1)^2}} }

where: R1 is the chosen radius of curvature for the right domain;

d_1 ~ = ~ sqrt{{R_1^2 + (r+t_sh)^2} - {2R_1 (r+t_sh)cos%delta_1}}

and	%delta_1 ~=~ %THETA_1 - ~arcsin left( {(r+t_sh) sin(180-%THETA_1)} over R right)

Domain outer curved cap (left):

F_l ^OC ~ = ~%DELTA%eta_d ~ 2%pi int from {-(r+t_sh)cos%THETA_2} to -R_2 + d_2 dz ~ e^{iQz cos%psi} ~ [R_2^2 - (z+d_2)^2] ~ {J_1 (Q sqrt{R_2^2 - (z+d_2)^2} sin%psi)} over {Q sqrt{R_2^2 - (z+d_2)^2}}

Inner curved cap (right):

F_rt^IC ~=~%DELTA%eta_d ~ 2%pi int from {(r+t_sh) cos%THETA_1 - L} to R_1-d_1 - L dz ~ e^{iQz cos%psi} ~ [R_1^2 - (z+d_1)^2]~ {J_1 (Q sqrt{R_1^2 - (z+d_1)^2} sin%psi)} over {Q sqrt{R_1^2 - (z+d_1)^2}}

Inner curved cap (left):

F_l^IC ~=~%DELTA%eta_d ~ 2%pi int from {-(r+t_sh) cos%THETA_2 + L} to -R_1+d_2 + L dz ~ e^{iQz cos%psi} ~ [R_2^2 - (z+d_2)^2]~ {J_1 (Q sqrt{R_2^2 - (z+d_2)^2} sin%psi)} over {Q sqrt{R_2^2 - (z+d_2)^2}}

Total Form factor = (2) - (1) - (3) - (4) + (5) + (6) + (7) + (8) - (9) - (10)